Table of Contents

1.Intorduction

2.What Is GPRS ?

3. Key User Features of GPRS

- Speed Immediacy

- New Applications

- Better Applications

- Service Access

4. Key Network Features of GPRS

- Packet Switching

- Spectrum Efficiency

- Internet Aware

5.GPRS Terminals

- GPRS Terminal Classes

- GPRS Telephones

- Data Transmission Speeds

6. GPRS Architecture

- GPRS Subscriber Terminals

- GPRS BSS

- GPRS Network

- GPRS Mobility Management

7. GPRS Data Communication

- Data Packet Routing

8. Limitations of GPRS

- Limited Cell Capacity For All Users

- Speeds Much Lower in Reality

- Suppoort of GPRS Mobile Terminate by Terminals is not Ensured

- Suboptimal Modulation

- Transit Delays

- No Store and Forward

9. Applications for GPRS

- Chat

- Textual and Visual Information

- Still Images

- Moving Images

- Web Browsing

- Document Sharing/ Collaborative Working

- Audio

- Job Dispatch

- Corporate Email

- Internet Email

- Vehicle Positioning

- Remote LAN Access

- File Transfer

- Home Automation

10.Related GPRS Challenges

- Billing

- Tariffing

- Customer Service

11. Glossary

12. References

Introduction

The idea of cell-based mobile radio systems appeared at Bell Laboratories, in the USA, in the early 1970s. However, it was not until a decade later that such systems were introduced for commercial use. During the early 1980s, analogue cellular telephone systems experienced a very rapid growth in Europe, particularly in Scandinavia and the United Kingdom. Cellular-phone systems use the 800MHz (806 to 902 MHz) and 1.9GHz (1,850 to 1,990 MHz) frequency bands. The 1.9GHz frequencies are allocated to PCS (personal communication services), but many cellular systems use these frequencies as they bundle PCS capabilities on their voice-centric service.

The early, first generation cellular systems were analogue and operated in the 800MHz frequencies. Later extensions operated at 1.8GHz and in parts of North America at 1.9GHz. The second generation (2G) appeared about 10 years later, with the first digital mobile, circuit-switched networks. These systems provided better voice quality, higher capacity, lower power requirements and global roaming capabilities. They operated in both the 800MHz and the PCS bands. But the advancements now…….

Everything is converging. The wired world and the wireless world are converging. The Internet and mobile wireless is converging. The distinction between the wireless, wireline and the Internet service providers is beginning to blur. And the glue certainly is "mobile wireless". Mobile wireless has exploded in popularity because of the fact that it simplifies and revolutionizes communication. The market for mobile wireless is increasing by leaps and bounds. The success of mobile communications lies in the ability to provide instant connectivity anytime and anywhere and the ability to provide high-speed data services to the mobile user. The quality and speeds available in the mobile environment must match the fixed networks if the convergence of the mobile wireless and fixed communication networks is to happen in the real sense. A range of successful mobile technologies exists today in various parts of the world and every technology must evolve to fulfill all these requirements.

The mobile wireless market is predominantly voice-oriented with low speed data services. The popularity of mobile voice services has been the deciding factor for the development of mobile networks so far. Data, mainly in the form of SMS has basically been an extra service. However, SMS is fast becoming very popular and in many European countries subscribers are spending more on SMS than voice. Although digital technologies have improved the quality of service provided by the mobile networks, the voice quality is still not the same as the toll quality. New speech coding techniques like EFR and adaptive multi-rate are bridging this gap.

Many second-generation mobile technologies exist today each having influence in specific parts of the world. GSM, TDMA (IS 136), and CDMA (IS 95) are the main technologies in the second-generation mobile market. GSM by far has been the most successful standard in terms of it's coverage. All these systems have different features and capabilities. Although both GSM and TDMA based networks use time division multiplexing on the air interfaces, their channel sizes, structures and core networks are different. CDMA has an entirely different air interface. The General Packet Radio System (GPRS) is a new service that provides actual packet radio access for mobile Global System for Mobile Communications (GSM) and time-division multiple access (TDMA) users

What is GPRS ?

GPRS is a packet-based data bearer service for GSM and TDMA networks. It is being rolled out by operators around the world as the first vital step towards 3G. GPRS gives mobile users faster data speeds and is particularly suitable for "bursty" Internet and intranet traffic. It makes mobile data faster, cheaper and more user-friendly than ever before. With GPRS-enabled mobile devices, users can be "always on" the Mobile Internet, so that, for example, emails arrive instantaneously. It also permits users to receive calls simultaneously when sending and receiving data calls.

GPRS can be implemented by simply adding new packet data nodes in GSM/TDMA networks, and upgrading existing nodes to provide a routing path for packet data between the mobile terminal and a gateway node. The gateway node provides interworking with external packet data networks for access to the Internet and intranets, for example, and requires few or no hardware upgrades to existing GSM/TDMA nodes.

Upgrades to existing GSM, GPRS and TDMA networks are planned that will allow single-slot rates of 38.4 Kbit/s for HSCSD and 60 Kbit/s for GPRS - allowing rates as high as 384 Kbit/s by joining multiple time slots. Known as Enhanced Data for GSM Evolution (EDGE) these upgrades represent the final evolution of data communications within the GSM standard and will enable operators with existing 2G networks to evolve to 3G services on existing network frequencies, using current network infrastructure.

GPRS is ideal for Wireless Application Protocol (WAP) services. WAP over GPRS brings cost savings to both mobile operators and consumers, because GPRS radio resources are only needed while transferring the message. For the end user, that means you only pay for the time it takes to download. WAP content is optimised for thin-client devices, such as mobile phones and is also future proof, enabling it to be deployed on 2.5G, 3G and other networks. While GPRS features efficient use of resources, instant access, fast delivery of information and innovative charging models. WAP and GPRS therefore represent a winning combination for the mobile end users, operators, service providers, enterprises as well as application developers.

The main objectives to be reached by implementing GPRS are the following:  
- give support for bursty traffic  
- use efficiently network and radio resources  
- provide flexible services at relatively low costs  
- possibility for connectivity to the Internet  
- provide fast access time  
- to have and support flexible co-existence with GSM voice

GPRS provides end-to-end IP connectivity that can be used to connect corporate LANs, ISPs and operators' own service LANs via interfaces to TCP/IP and X.25. GPRS gives almost instantaneous connection set-up, and allows charging on the basis of data transmitted rather than connection time. As a packet data technology, GPRS only uses network resources and bandwidth when data is actually transmitted. This makes extremely efficient use of available radio bandwidth. Supported data rates range from 14.4 Kbps using just one TDMA slot, up to 115 Kbps and higher using all eight.

In order to meet these objectives the following technologies are applied. GPRS uses a packet-mode technique to transfer data and signaling in a cost-efficient manner over GSM radio networks and also optimizes the use of radio and network resources. Still a strict separation between the radio and network subsystems is maintained in order to allow the network subsystem to be reused with other radio access technologies.

New GPRS radio channels are also defined. The allocation of these timeslots is flexible, ranging from one to eight timeslots per TDMA frame, and they can be shared by active users. This allows GPRS to handle bitrates from 9 to even up to 150 kbit/s per user. With these bit rates all types of transmissions can be handled: from slow-speed short messages to the higher speeds needed e.g. when browsing Web pages. GPRS will also permit the user to receive voice calls simultaneously when sending or receiving data calls.

GPRS will provide a seamless connection to the existing standard data services by using interfaces to TCP/IP and X.25. GPRS will also provide fast reservation to begin transmission of packets, typically from 0,5 to 1 second. This means that the data users will not have to wait for the phone to dial, but instead they will get through immediately. For example the messages will be delivered direct to the user's phone, without the need for a full end-to-end connection. When the user switches on their phone, the message will be downloaded automatically.

The GPRS services will reflect the GSM services with an exception that the GPRS will have a tremendous transmission rate which will make a good impact in the most of the existing services and a possibility of introduction of new services as operators and users (business/private) appreciate the newly introduced technology.

Services such as the Internet, videoconferencing and on-line shopping will be as smooth as talking on the phone, moreover we'll be able to access these services whether we are at work, at home or travelling.

In the new information age, the mobile phone will deliver much than just voice calls. It will become a multi-media communications device, capable of sending and receiving graphic images and video.

Key User Features of GPRS

The General Packet Radio Service (GPRS) is a new nonvoice value added service that allows information to be sent and received across a mobile telephone network. It supplements today's Circuit Switched Data and Short Message Service. GPRS is NOT related to GPS (the Global Positioning System), a similar acronym that is often used in mobile contexts. GPRS has several unique features which can be summarized as:

SPEED

Theoretical maximum speeds of up to 171.2 kilobits per second (kbps) are achievable with GPRS using all eight timeslots at the same time. This is about three times as fast as the data transmission speeds possible over today's fixed telecommunications networks and ten times as fast as current Circuit Switched Data services on GSM networks. By allowing information to be transmitted more quickly, immediately and efficiently across the mobile network, GPRS may well be a relatively less costly mobile data service compared to SMS and Circuit Switched Data.

IMMEDIACY

GPRS facilitates instant connections whereby information can be sent or received immediately as the need arises, subject to radio coverage. No dial-up modem connection is necessary. This is why GPRS users are sometimes referred to be as being "always connected". Immediacy is one of the advantages of GPRS (and SMS) when compared to Circuit Switched Data. High immediacy is a very important feature for time critical applications such as remote credit card authorization where it would be unacceptable to keep the customer waiting for even thirty extra seconds.

NEW APPLICATIONS, BETTER APPLICATIONS

GPRS facilitates several new applications that have not previously been available over GSM networks due to the limitations in speed of Circuit Switched Data (9.6 kbps) and message length of the Short Message Service (160 characters). GPRS will fully enable the Internet applications you are used to on your desktop from web browsing to chat over the mobile network. Other new applications for GPRS, profiled later, include file transfer and home automation- the ability to remotely access and control in-house appliances and machines.

#### SERVICE ACCESS

To use GPRS users specifically need following things. A mobile phone or terminal that supports GPRS (existing GSM phones do NOT support GPRS), a subscription to a mobile telephone network that supports GPRS, use of GPRS must be enabled for that user. Automatic access to the GPRS may be allowed by some mobile network operators, others will require a specific opt-in. Knowledge of how to send and/ or receive GPRS information using their specific model of mobile phone, including software and hardware configuration (this creates a customer service requirement). A destination to send or receive information through GPRS. Whereas with SMS this was often another mobile phone, in the case of GPRS, it is likely to be an Internet address, since GPRS is designed to make the Internet fully available to mobile users for the first time. From day one, GPRS users can access any web page or other Internet applications- providing an immediate critical mass of uses.

Key Network Features of GPRS

PACKET SWITCHING

GPRS involves overlaying a packet based air interface on the existing circuit switched GSM network. This gives the user an option to use a packet-based data service. To supplement a circuit switched network architecture with packet switching is quite a major upgrade. However, as we shall see later, the GPRS standard is delivered in a very elegant manner- with network operators needing only to add a couple of new infrastructure nodes and making a software upgrade to some existing network elements.

With GPRS, the information is split into separate but related "packets" before being transmitted and reassembled at the receiving end. Packet switching is similar to a jigsaw puzzle- the image that the puzzle represents is divided into pieces at the manufacturing factory and put into a plastic bag. During transportation of the now boxed jigsaw from the factory to the end user, the pieces get jumbled up. When the recipient empties the bag with all the pieces, they are reassembled to form the original image. All the pieces are all related and fit together, but the way they are transported and assembled varies. The Internet itself is another example of a packet data network, the most famous of many such network types.

SPECTRUM EFFICIENCY

Packet switching means that GPRS radio resources are used only when users are actually sending or receiving data. Rather than dedicating a radio channel to a mobile data user for a fixed period of time, the available radio resource can be concurrently shared between several users. This efficient use of scarce radio resources means that large numbers of GPRS users can potentially share the same bandwidth and be served from a single cell. The actual number of users supported depends on the application being used and how much data is being transferred. Because of the spectrum efficiency of GPRS, there is less need to build in idle capacity that is only used in peak hours. GPRS therefore lets network operators maximize the use of their network resources in a dynamic and flexible way, along with user access to resources and revenues.

GPRS should improve the peak time capacity of a GSM network since it simultaneously:                   i) Allocates scarce radio resources more efficiently by supporting virtual connectivity

ii)Imigrates traffic that was previously sent using Circuit Switched Data to GPRS instead, and reduces SMS Center and signaling channel loading by migrating some traffic that previously was sent using SMS to GPRS instead using the GPRS / SMS interconnect that is supported by the GPRS standards. 
INTERNET AWARE

For the first time, GPRS fully enables Mobile Internet functionality by allowing interworking between the existing Internet and the new GPRS network. Any service that is used over the fixed Internet today- File Transfer Protocol (FTP), web browsing, chat, email, telnet- will be as available over the mobile network because of GPRS. In fact, many network operators are considering the opportunity to use GPRS to help become wireless Internet Service Providers in their own right.

The World Wide Web is becoming the primary communications interface- people access the Internet for entertainment and information collection, the intranet for accessing company information and connecting with colleagues and the extranet for accessing customers and suppliers. These are all derivatives of the World Wide Web aimed at connecting different communities of interest.Because it uses the same protocols, the GPRS network can be viewed as a sub-network of the Internet with GPRS capable mobile phones being viewed as mobile hosts. This means that each GPRS terminal can potentially have its own IP address and will be addressable as such.

SUPPORTS TDMA AND GSM

It should be noted right that the General Packet Radio Service is not only a service designed to be deployed on mobile networks that are based on the GSM digital mobile phone standard. The IS-136 Time Division Multiple Access (TDMA) standard, popular in North and South America, will also support GPRS. This follows an agreement to follow the same evolution path towards third generation mobile phone networks concluded in early 1999 by the industry associations that support these two network types.

##### GPRS Terminals

A complete understanding of the application availability and GPRS timeline requires understanding of terminal types and availability. The term "terminal equipment" is generally used to refer to the variety of mobile phones and mobile stations that can be used in a GPRS environment; the equipment is defined by terminal classes and types. GPRS Terminal Classes

A GPRS terminal can be one of three classes: A, B, or C. A Class A terminal supports GPRS and other GSM services (such as SMS and voice) simultaneously. This support includes simultaneous attach, activation, monitor, and traffic. As such, a Class A terminal can make or receive calls on two services simultaneously. In the presence of circuit-switched services, GPRS virtual circuits will be held or placed on busy rather than being cleared.

A Class B terminal can monitor GSM and GPRS channels simultaneously, but can support only one of these services at a time. Therefore, a Class B terminal can support simultaneous attach, activation, and monitor, but not simultaneous traffic. As with Class A, the GPRS virtual circuits will not be closed down when circuit-switched traffic is present. Instead, they will be switched to busy or held mode. Thus, users can make or receive calls on either a packet or a switched call type sequentially, but not simultaneously.

A Class C terminal supports only nonsimultaneous attach. The user must select which service to connect to. Therefore, a Class C terminal can make or receive calls from only the manually (or default) selected service. The service that is not selected is not reachable. Finally, the GPRS specifications state that support of SMS is optional for Class C terminals.

GPRS Telephones

Owing to the fact that more than one channel is used for downlink, the GPRS mobile phones make possible greater data transmission speeds. There are several types of phones with regard to the number of channels they use for data transmission...

Type 2+1 – two downlink channels and one uplink data transmission channel

Type 3+1 – three downlink channels and one uplink data transmission channel

Type 4+1 – four downlink channels and one uplink data transmission channel

Data Transmission Speeds

The supported data transmission speed per channel is 13.4Kbits. Depending on the type of phone, the following data transmission speeds are theoretically possible...

Type 2+1: Receive 26.8Kbits and send 13.4Kbits.

Type 3+1: Receive 40.2Kbits and send 13.4Kbits.

Type 4+1: Receive 53.6Kbits and send 13.4Kbits.

##### GPRS Architecture

From a high level, GPRS can be thought of as an overlay network onto a second-generation GSM network. This data overlay network provides packet data transport at rates from 9.6 to 171 kbps. Additionally, multiple users can share the same air-interface resources.

GPRS attempts to reuse the existing GSM network elements as much as possible, but in order to effectively build a packet-based mobile cellular network, some new network elements, interfaces, and protocols that handle packet traffic are required. Therefore, GPRS requires modifications to numerous network elements, as summarized in Table

Table : Modifications Required for GPRS

| GSM Network Element | Modification or Upgrade Required for GPRS |
| --- | --- |
| Subscriber Terminal (TE) | A totally new subscriber terminal is required to access GPRS services. These new terminals will be backward compatible with GSM for voice calls. |
| BTS | A software upgrade is required in the existing base transceiver site (BTS). |
| BSC | The base station controller (BSC) will also require a software upgrade, as well as the installation of a new piece of hardware called a packet control unit (PCU). The PCU directs the data traffic to the GPRS network and can be a separate hardware element associated with the BSC. |
| Core Network | The deployment of GPRS requires the installation of new core network elements called the Serving GPRS Support Node (SGSN) and Gateway GPRS Support Node (GGSN). |
| Databases (VLR, HLR, and so on) | All the databases involved in the network will require software upgrades to handle the new call models and functions introduced by GPRS. |

#### GPRS Subscriber Terminals

New terminals (TEs) are required because existing GSM phones do not handle the enhanced air interface, nor do they have the ability to packetize traffic directly. A variety of terminals will exist, as described in a previous section, including a high-speed version of current phones to support high-speed data access, a new kind of PDA device with an embedded GSM phone, and PC Cards for laptop computers. All these TEs will be backward compatible with GSM for making voice calls using GSM.

#### GPRS BSS

Each BSC will require the installation of one or more PCUs and a software upgrade. The PCU provides a physical and logical data interface out of the base station system (BSS) for packet data traffic. The BTS may also require a software upgrade, but typically will not require hardware enhancements.

When either voice or data traffic is originated at the subscriber terminal, it is transported over the air interface to the BTS, and from the BTS to the BSC in the same way as a standard GSM call. However, at the output of the BSC the traffic is separated; voice is sent to the mobile switching center (MSC) per standard GSM, and data is sent to a new device called the SGSN, via the PCU over a Frame Relay interface.

Figure : Generic GPRS Network Architecture

#### GPRS Network

In the core network, the existing MSCs are based upon circuit-switched central-office technology, and they cannot handle packet traffic. Thus two new components, called GPRS Support Nodes, are added:

Serving GPRS Support Node (SGSN)

Gateway GPRS Support Node (GGSN)

The SGSN can be viewed as a "packet-switched MSC;" it delivers packets to mobile stations (MSs) within its service area. SGSNs send queries to home location registers (HLRs) to obtain profile data of GPRS subscribers. SGSNs detect new GPRS MSs in a given service area, process registration of new mobile subscribers, and keep a record of their location inside a given area. Therefore, the SGSN performs mobility management functions such as mobile subscriber attach/detach and location management. The SGSN is connected to the base-station subsystem via a Frame Relay connection to the PCU in the BSC.

GGSNs are used as interfaces to external IP networks such as the public Internet, other mobile service providers' GPRS services, or enterprise intranets. GGSNs maintain routing information that is necessary to tunnel the protocol data units (PDUs) to the SGSNs that service particular MSs. Other functions include network and subscriber screening and address mapping. One (or more) GGSNs may be provided to support multiple SGSNs. More detailed technical descriptions of the SGSN and GGSN are provided in a later section.

#### GPRS Mobility Management

Mobility management within GPRS builds on the mechanisms used in GSM networks; as a MS moves from one area to another, mobility management functions are used to track its location within each mobile network. The SGSNs communicate with each other and update the user location. The MS profiles are preserved in the visitor location registers (VLRs) that are accessible by the SGSNs via the local GSM MSC. A logical link is established and maintained between the MS and the SGSN in each mobile network. At the end of transmission or when a MS moves out of the area of a specific SGSN, the logical link is released and the resources associated with it can be reallocated.

The operation of the GPRS is partly independent of the GSM network. However, some procedures share the network elements with current GSM functions to increase efficiency and to make optimum use of free GSM resources (such as unallocated time slots).

Figure : States of GPRS in a Mobile Station

An MS has three states in the GPRS system: idle, standby, and active. The three-state model represents the nature of packet radio relative to the GSM two-state model (idle or active).

Data is transmitted between a MS and the GPRS network only when the MS is in the active state. In the active state, the SGSN knows the cell location of the MS. However, in the standby state, the location of the MS is known only as to which routing area it is in. (The routing area can consist of one or more cells within a GSM location area.)

When the SGSN sends a packet to a MS that is in the standby state, the MS must be paged. Because the SGSN knows the routing area in which the MS is located, a packet paging message is sent to that routing area. After receiving the packet paging message, the MS gives its cell location to the SGSN to establish the active state.

Packet transmission to an active MS is initiated by packet paging to notify the MS of an incoming data packet. The data transmission proceeds immediately after packet paging through the channel indicated by the paging message. The purpose of the packet paging message is to simplify the process of receiving packets. The MS has to listen to only the packet paging messages, instead of all the data packets in the downlink channels, reducing battery use significantly.

When an MS has a packet to be transmitted, access to the uplink channel is needed. The uplink channel is shared by a number of MSs, and its use is allocated by a BSS. The MS requests use of the channel in a packet random access message. The transmission of the packet random access message follows Slotted Aloha procedures. The BSS allocates an unused channel to the MS and sends a packet access grant message in reply to the packet random access message. The description of the channel (one or multiple time slots) is included in the packet access grant message. The data is transmitted on the reserved channels.

The main reasons for the standby state are to reduce the load in the GPRS network caused by cell-based routing update messages and to conserve the MS battery. When a MS is in the standby state, there is no need to inform the SGSN of every cell change—only of every routing area change. The operator can define the size of the routing area and, in this way, adjust the number of routing update messages.

In the idle state, the MS does not have a logical GPRS context activated or any Packet-Switched Public Data Network (PSPDN) addresses allocated. In this state, the MS can receive only those multicast messages that can be received by any GPRS MS. Because the GPRS network infrastructure does not know the location of the MS, it is not possible to send messages to the MS from external data networks.

A cell-based routing update procedure is invoked when an active MS enters a new cell. In this case, the MS sends a short message containing information about its move (the message contains the identity of the MS and its new location) through GPRS channels to its current SGSN. This procedure is used only when the MS is in the active state.

When an MS in an active or a standby state moves from one routing area to another in the service area of one SGSN, it must again perform a routing update. The routing area information in the SGSN is updated and the success of the procedure is indicated in the response message.

The inter-SGSN routing update is the most complicated of the three routing updates. In this case, the MS changes from one SGSN area to another, and it must establish a new connection to a new SGSN. This means creating a new logical link context between the MS and the new SGSN, as well as informing the GGSN about the new location of the MS.

##### GPRS Data Communication

Some cooperation still exists between elements of the current GSM services and GPRS. On the physical layer, resources can be reused and some common signaling issues exist. In the same radio carrier, there can be time slots (TSs) reserved simultaneously for circuit-switched and GPRS use. The most optimum resource utilization is obtained through dynamic sharing between circuit-switched and GPRS channels. During the establishment of a circuit-switched call, there is enough time to preempt the GPRS resources for circuit-switched calls that have higher priority.

One of the main issues in the GPRS network is the routing of data packets to/from a mobile user. The issue can be divided into two areas: data packet routing and mobility management.

Data Packet Routing

The main functions of the GGSN involve interaction with the external data network. The GGSN updates the location directory using routing information supplied by the SGSNs about the location of a MS and routes the external data network protocol packet encapsulated over the GPRS backbone to the SGSN currently serving the MS. It also decapsulates and forwards external data network packets to the appropriate data network and collects charging data that is forwarded to a charging gateway.

Limitations of GPRS

It should already be clear that GPRS is an important new enabling mobile data service which offers a major improvement in spectrum efficiency, capability and functionality compared with today's nonvoice mobile services. However, it is important to note that there are some limitations with GPRS, which can be summarized as:

LIMITED CELL CAPACITY FOR ALL USERS

GPRS does impact a network's existing cell capacity. There are only limited radio resources that can be deployed for different uses- use for one purpose precludes simultaneous use for another. For example, voice and GPRS calls both use the same network resources. The extent of the impact depends upon the number of timeslots, if any, that are reserved for exclusive use of GPRS. However, GPRS does dynamically manage channel allocation and allow a reduction in peak time signalling channel loading by sending short messages over GPRS channels instead.

RESULT: NEED FOR SMS as a complementary bearer that uses a different type of radio resource.

SPEEDS MUCH LOWER IN REALITY

Achieving the theoretical maximum GPRS data transmission speed of 172.2 kbps would require a single user taking over all eight timeslots without any error protection. Clearly, it is unlikely that a network operator will allow all timeslots to be used by a single GPRS user. Additionally, the initial GPRS terminals are expected be severely limited- supporting only one, two or three timeslots. The bandwidth available to a GPRS user will therefore be severely limited. As such, the theoretical maximum GPRS speeds should be checked against the reality of constraints in the networks and terminals. The reality is that mobile networks are always likely to have lower data transmission speeds than fixed networks.

RESULT: Relatively high mobile data speeds may not be available to individual mobile users until Enhanced Data rates for GSM Evolution (EDGE) or Universal Mobile Telephone System (3GSM) are introduced.

SUPPORT OF GPRS MOBILE TERMINATE BY TERMINALS IS NOT ENSURED

At the time of writing, there has been no confirmation from any handset vendors that mobile terminated GPRS calls (i.e. receipt of GPRS calls on the mobile phone) will be supported by the initial  GPRS terminals. Availability or not of GPRS MT is a central question with critical impact on the GPRS business case such as application migration from other nonvoice bearers.

By originating the GPRS session, users confirm their agreement to pay for the delivery of content from that service. This origination may well be performed using a Wireless Application Protocol (WAP) session using the WAP microbrowser that will be built into GHPRS terminals. However, mobile terminated IP traffic might allow unsolicited information to reach the terminal. Internet sources originating such unsolicited content may not be chargeable. A possible worse case scenario would be that mobile users would have to pay for receiving unsolicited junk content. This is a potential reason for a mobile vendor NOT to support GPRS Mobile Terminate in their GPRS terminals.

However, there is always the possibility of unsolicited or unwanted information being communicated through any media, but that does not mean that we would wish to preclude the possibility of any kind of communication through that means altogether. A network side solution such as GGSN or charging platform policing would be preferable rather than a non-flexible limitation built into all the GPRS handsets.

RESULT: GPRS usability and therefore business case is threatened if GPRS MT is not supported by GPRS terminals.

SUBOPTIMAL MODULATION

GPRS is based on a modulation technique known as Gaussian minimum-shift keying (GMSK). EDGE is based on a new modulation scheme that allows a much higher bit rate across the air interface- this is called eight-phase-shift keying (8 PSK) modulation. Since 8 PSK will also be used for 3GSM, network operators will need to incorporate it at some stage to make the transition to third generation mobile phone systems.

RESULT: NEED FOR EDGE.

TRANSIT DELAYS

GPRS packets are sent in all different directions to reach the same destination. This opens up the potential for one or some of those packets to be lost or corrupted during the data transmission over the radio link. The GPRS standards recognize this inherent feature of wireless packet technologies and incorporate data integrity and retransmission strategies. However, the result is that potential transit delays can occur.

Because of this, applications requiring broadcast quality video may well be implemented using High Speed Circuit Switched Data (HSCSD). HSCSD is simply a Circuit Switched Data call in which a single user can take over up to four separate channels at the same time. Because of its characteristic of end to end connection between sender and recipient, transmission delays are less likely.

RESULT: NEED FOR HSCSD.

NO STORE AND FORWARD

Whereas the Store and Forward Engine in the Short Message Service is the heart of the SMS Center and key feature of the SMS service, there is no storage mechanism incorporated into the GPRS standard, apart from the incorporation of interconnection links between SMS and GPRS.

Applications for GPRS

A wide range of corporate and consumer applications are enabled by nonvoice mobile services such as SMS and GPRS. This section will introduce those that are particularly suited to GPRS.

CHAT

Chat can be distinguished from general information services because the source of the information is a person with chat whereas it tends to be from an Internet site for information services. The "information intensity"- the amount of information transferred per message tends to be lower with chat, where people are more likely to state opinions than factual data. In the same way as Internet chat groups have proven a very popular application of the Internet, groups of likeminded people- so called communities of interest- have begun to use nonvoice mobile services as a means to chat and communicate and discuss.

Because of its synergy with the Internet, GPRS would allow mobile users to participate fully in existing Internet chat groups rather than needing to set up their own groups that are dedicated to mobile users. Since the number of participants is an important factor determining the value of participation in the newsgroup, the use of GPRS here would be advantageous. GPRS will not however support point to multipoint services in its first phase, hindering the distribution of a single message to a group of people. As such, given the installed base of SMS capable devices, we would expect SMS to remain the primary bearer for chat applications in the foreseeable future, although experimentation with using GPRS is likely to commence sooner rather than later.

TEXTUAL AND VISUAL INFORMATION

A wide range of content can be delivered to mobile phone users ranging from share prices, sports scores, weather, flight information, news headlines, prayer reminders, lottery results, jokes, horoscopes, traffic, location sensitive services and so on. This information need not necessarily be textual- it may be maps or graphs or other types of visual information.

The length of a short message of 160 characters suffices for delivering information when it is quantitative- such as a share price or a sports score or temperature. When the information is of a qualitative nature however, such as a horoscope or news story, 160 characters is too short other than to tantalize or annoy the information recipient since they receive the headline or forecast but little else of substance. As such, GPRS will likely be used for qualitative information services when end users have GPRS capable devices, but SMS will continue to be used for delivering most quantitative information services. Interestingly, chat applications are a form of qualitative information that may remain delivered using SMS, in order to limit people to brevity and reduce the incidence of spurious and irrelevant posts to the mailing list that are a common occurrence on Internet chat groups.

STILL IMAGES

Still images such as photographs, pictures, postcards, greeting cards and presentations, static web pages can be sent and received over the mobile network as they are across fixed telephone networks. It will be possible with GPRS to post images from a digital camera connected to a GPRS radio device directly to an Internet site, allowing near real-time desktop publishing.

MOVING IMAGES

Over time, the nature and form of mobile communication is getting less textual and more visual. The wireless industry is moving from text messages to icons and picture messages to photographs and blueprints to video messages and movie previews being downloaded and on to full blown movie watching via data streaming on a mobile device.

Sending moving images in a mobile environment has several vertical market applications including monitoring parking lots or building sites for intruders or thieves, and sending images of patients from an ambulance to a hospital. Videoconferencing applications, in which teams of distributed sales people can have a regular sales meeting without having to go to a particular physical location, is another application for moving images.

WEB BROWSING

Using Circuit Switched Data for web browsing has never been an enduring application for mobile users. Because of the slow speed of Circuit Switched Data, it takes a long time for data to arrive from the Internet server to the browser. Alternatively, users switch off the images and just access the text on the web, and end up with difficult to read text layouts on screens that are difficult to read from. As such, mobile Internet browsing is better suited to GPRS.

DOCUMENT SHARING/ COLLABORATIVE WORKING

Mobile data facilitates document sharing and remote collaborative working. This lets different people in different places work on the same document at the same time. Multimedia applications combining voice, text, pictures and images can even be envisaged. These kinds of applications could be useful in any problem solving exercise such as fire fighting, combat to plan the route of attack, medical treatment, advertising copy setting, architecture, journalism and so on. Even comments on which resort to book a holiday at could benefit from document sharing to save everyone having to visit the travel agent to make a decision. Anywhere somebody can benefit from having and being able to comment on a visual depiction of a situation or matter, such collaborative working can be useful. By providing sufficient bandwidth, GPRS facilitates multimedia applications such as document sharing.

AUDIO

Despite many improvements in the quality of voice calls on mobile networks such as Enhanced Full Rate (EFR), they are still not broadcast quality. There are scenarios where journalists or undercover police officers with portable professional broadcast quality microphones and amplifiers capture interviews with people or radio reports dictated by themselves and need to send this information back to their radio or police station. Leaving a mobile phone on, or dictating to a mobile phone, would simply not give sufficient voice quality to allow that transmission to be broadcast or analyzed for the purposes of background noise analysis or voice printing, where the speech autograph is taken and matched against those in police storage. Since even short voice clips occupy large file sizes, GPRS or other high speed mobile data services are needed.

JOB DISPATCH

Nonvoice mobile services can be used to assign and communicate new jobs from office-based staff to mobile field staff. Customers typically telephone a call center whose staff take the call and categorize it. Those calls requiring a visit by field sales or service representative can then be escalated to those mobile workers. Job dispatch applications can optionally be combined with vehicle positioning applications- such that the nearest available suitable personnel can be deployed to serve a customer.

CORPORATE EMAIL

With up to half of employees typically away from their desks at any one time, it is important for them to keep in touch with the office by extending the use of corporate email systems beyond an employee's office PC. Corporate email systems run on Local

Area computer Networks (LAN) and include Microsoft Mail, Outlook, Outlook Express, Microsoft Exchange, Lotus Notes and Lotus cc:Mail.

Since GPRS capable devices will be more widespread in corporations than amongst the general mobile phone user community, there are likely to be more corporate email applications using GPRS than Internet email ones whose target market is more general.

INTERNET EMAIL

Internet email services come in the form of a gateway service where the messages are not stored, or mailbox services in which messages are stored. In the case of gateway services, the wireless email platform simply translates the message from SMTP, the Internet email protocol, into SMS and sends to the SMS Center. In the case of mailbox email services, the emails are actually stored and the user gets a notification on their mobile phone and can then retrieve the full email by dialing in to collect it, forward it and so on.

Upon receiving a new email, most Internet email users do not currently get notified of this fact on their mobile phone. When they are out of the office, they have to dial in speculatively and periodically to check their mailbox contents. However, by linking Internet email with an alert mechanism such as SMS or GPRS, users can be notified when a new email is received.

VEHICLE POSITIONING

This application integrates satellite positioning systems that tell people where they are with nonvoice mobile services that let people tell others where they are. The Global Positioning System (GPS) is a free-to-use global network of 24 satellites run by the US Department of Defense. Anyone with a GPS receiver can receive their satellite position and thereby find out where they are. Vehicle positioning applications can be used to deliver several services including remote vehicle diagnostics, ad-hoc stolen vehicle tracking and new rental car fleet tariffs.

The Short Message Service is ideal for sending Global Positioning System (GPS) position information such as longitude, latitude, bearing and altitude. GPS coordinates are typically about 60 characters in length. GPRS could alternatively be used.

REMOTE LAN ACCESS

When mobile workers are away from their desks, they clearly need to connect to the Local Area Network in their office. Remote LAN applications encompasses access to any applications that an employee would use when sitting at their desk, such as access to the intranet, their corporate email services such as Microsoft Exchange or Lotus Notes and to database applications running on Oracle or Sybase or whatever. The mobile terminal such as handheld or laptop computer has the same software programs as the desktop on it, or cut down client versions of the applications accessible through

the corporate LAN. This application area is therefore likely to be a conglomeration of remote access to several different information types- email, intranet, databases. This information may all be accessible through web browsing tools, or require proprietary software applications on the mobile device. The ideal bearer for Remote LAN Access depends on the amount of data being transmitted, but the speed and latency of GPRS make it ideal.

FILE TRANSFER

As this generic term suggests, file transfer applications encompass any form of downloading sizeable data across the mobile network. This data could be a presentation document for a traveling salesperson, an appliance manual for a service engineer or a software application such as Adobe Acrobat Reader to read documents. The source of this information could be one of the Internet communication methods such as FTP (File Transfer Protocol), telnet, http or Java- or from a proprietary database or legacy platform. Irrespective of source and type of file being transferred, this kind of application tends to be bandwidth intensive. It therefore requires a high speed mobile data service such as GPRS, EDGE or 3GSM to run satisfactorily across a mobile network.

HOME AUTOMATION

Home automation applications combine remote security with remote control. Basically, you can monitor your home from wherever you are- on the road, on holiday, or at the office. If your burglar alarm goes off, not only do you get alerted, but you get to go live and see who are perpetrators are and perhaps even lock them in. Not only can you see things at home, but you can do things too. You can program your video, switch your oven on so that the preheating is complete by the time you arrive home (traffic jams permitting) and so on. Your GPRS capable mobile phone really does become like the remote control devices we use today for our television, video, hi-fi and so on. As the Internet Protocol (IP) will soon be everywhere- not just in mobile phones because of GPRS but all manner of household appliances and in every machine- these devices can be addressed and instructed. A key enabler for home automation applications will be Bluetooth, which allows disparate devices to interwork.

Related GPRS Challenges

BILLING

GPRS is a different kind of service from those typically available on today’s mobile networks. GPRS is essentially a packet switching overlay on a circuit switching network. The GPRS specifications stipulate the minimum charging information that must be collected in the Stage 1 service description. These include destination and source addresses, usage of radio interface, usage of external Packet Data Networks, usage of the packet data protocol addresses, usage of general GPRS resources and location of the Mobile Station. Since GPRS networks break the information to be communicated down into packets, at a minimum, a GPRS network needs to be able to count packets to charging customers for the volume of packets they send and receive. Today's billing systems have difficulties handling charging for today's nonvoice services. It is unlikely that circuit switched billing systems will be able to process a large number of new variables created by GPRS.

GPRS call records are generated in the GPRS Service Nodes. The GGSN and SGSN may not be able to store charging information but this charging information needs to be processed. However, the crucial challenge of being able to bill for GPRS and therefore earn a return on investment in GPRS is simplified by the fact that the major GPRS infrastructure vendors all support charging functions as part of their GPRS solutions. Additionally, a wide range of other existing non-GSM packet data networks such as X.25 and Cellular Digital Packet Data (CDPD) are in place along with associated billing systems.

It may well be the case that the cost of measuring packets is greater than their value. The implication is that there will NOT be a per packet charge since there may be too many packets to warrant counting and charging for.

TARIFFING

Decisions on charging for GPRS by packet or simply a flat monthly fee are contentious but need to be made. Charging different packets at different rates can make things complicated for the user, whilst flat rates favor heavy users more than occasional ones.

We believe that the optimal GPRS pricing model will be based on two variables- time and packet. Network operators should levy a nominal per packet charge during peak times plus a flat rate, no per packet charge during non peak times. Time and packet related charging will encourage applications such as remote monitoring, meter reading and chat to use GPRS overnight when spare network capacity is available. Simultaneously, a nominal per packet charge during the day will help to allocate scarce radio resources and charge radio heavy applications such as file and image transfer more than applications with lower data intensity. It has the advantage that it will automatically adjust customer charging according to their application usage.

As such the optimal charging model could well be a flat rate charge during off-peak times along with a per packet charge during peak times.

CUSTOMER SERVICE

Value-added network services such as mobile data, mobile Internet and unified messaging all generate certain specific customer problems and requirements, thereby requiring customer service personnel to be aware of these issues and know how to solve them.

Nonvoice services are surprisingly complex- involving unique configurations of phone types, data cards, handheld computers, subscriptions, operating systems, Internet service providers and so on. Some network operators require customers to opt into certain value added services rather than including them as part of the core subscription- necessitating a customer service process. It is even possible to write a 350 page book about the SHORT message service (it is called "YES2SMS")!In theory, the need for dedicated customer service for Circuit Switched Data, SMS and other nonvoice mobile services will decrease in the future as terminals and services become easier to use and as the services themselves are used more widely for customer service purposes.

The reality in the short and medium term is that the need for customer support for value-added services will increase not decrease as awareness of services and their usage increases, and as new services and terminals come onto the marketplace.

Rather than keeping everything in-house or outsourcing everything, we are a proponent of an approach that keeps first line support and customer contact in-house, whilst outsourcing the difficult specific customer service problems arising from connectivity issues and so on. In this way, the network operator is aware of and in control of the kinds of questions and problems its customers are asking.

It is well worth incurring the cost to get the customer aware, educated and initially set up with data services, because, for example, once the PC data card has been successfully connected to the laptop to the Internet software and so on, the same configuration can be repeatedly used. The one-off customer requirement leads to ongoing usage.

Glossary

| 2G | Second generation; generic name for second generation of digital mobile networks (such as GSM, and so on) |
| --- | --- |
| 3G | Third generation; generic name for next-generation mobile networks (Universal Telecommunications System [UMTS], IMT-2000; sometimes GPRS is called 3G in North America) |
| bps | Bits per second |
| BSC | Base Station Controller |
| BTS | Base transceiver station |
| CS | Circuit switched |
| EDGE | Enhanced data rates for GSM evolution; upgrade to GPRS systems that requires new base stations and claims to increase bandwidth to 384 kbps |
| ETSI | European Telecommunications Standards Institute |
| Gb | Interface between a SGSN and a BSS |
| Gc | Interface between a GGSN and a HLR |
| Gd | Interface between a SMS-GMSC and a SGSN, and between a SMS-IWMSC and a SGSN |
| Gf | Interface between a SGSN and an EIR |
| GGSN | Gateway GPRS Support Node |
| Gi | Reference point between GPRS and an external packet data network |
| GMSC | Gateway mobile services switching center |
| Gn | Interface between two GSNs within the same PLMN |
| Gp | Interface between two GSNs in different PLMNs |
| GPRS | General Packet Radio Service; upgrade to existing 2G digital mobile networks to provide higher-speed data services |
| Gr | Interface between a SGSN and a HLR |
| Gs | Interface between a SGSN and a MSC/VLR |
| GSM | Global System for Mobile Communications; most widely deployed 2G digital cellular mobile network standard |
| GSN | GPRS Support Node (xGSN) |
| GW | Gateway |
| HDLC | High-Level Data Link Control |
| HLR | Home location register |
| HSCSD | High-speed circuit-switched data; software upgrade for cellular networks that gives each subscriber 56K data |
| IP | Internet Protocol |
| ISP | Internet service provider |
| LLC | Logical Link Control |
| MAC | Medium Access Control |
| MM | Mobility management |
| MS | Mobile station |
| MSC | Mobile services switching center |
| NAS | Network access server |
| PCU | Packet control unit |
| PDA | Personal digital assistant |
| PDN | Packet data network |
| PDP | Packet Data Protocol |
| PSTN | Public Switched Telephone Network |
| SGSN | Serving GPRS Support Node |
| SMS | Short message service |
| SMSC | Short message service center |
| TCP | Transmission Control Protocol |
| TE | Terminal equipment |
| TDMA | Narrowband digital TDMA standard; uses same frequencies as AMPS, thus is also known as D-AMPS or digital AMPS |
| TS | Time slot |
| Um | Interface between the MS and the GPRS fixed network part |
| VLR | Visitor location register |
| WAP | Wireless access Protocol; important protocol stack (Layers 4 through 7 of the OSI model), used to send simplified Web pages to wireless devices; uses IP but replaces TCP and Hypertext Transfer Protocol (HTTP) with UDP and WTP, and requires pages to be written in WML rather than in HTML |

References

Wi-Bing Lin, Imrich Chlamtac, “Wireless and Mobile Network Architectures”

Chetan Sharma, “Wireless Internet Enterprise Application”

Behrouz A. Forouzan, “Data Communication & Networking “

Andrew S. Tenenbaum, “Computer Networks”

http://www.webopdia.com

http://www.wirelessdevnet.com/channels/wireless/training/mobilewirelesstoday2.html

http://www.3gpp.org/intro.htm

http://www.gsmworld.com/technology/top.htm

http://www.gsmworld.com/technology/gprs/intro.htm

http://www.forums.pctechguide.com/restricted/gprs/

http://www.cisco.com/whitepaper/gprs/